MP FLEX

_____________________________________________________________________________mplifts.com

CHARACTERISTICS

Type:					Gearless lift

Load:					180 kg up to 630 kg

Capacity:				From 2 to 8 passengers

Speed:					1m/s

Suspension:				1:1

Travel:					Up to 45 m.

Stops:					16 stops

Entrances:	Single entrance, double 180º entrance, double 90º entrance and triple entrance.

CAR

Model:					MP CARevolution, C and D series

CAR DOORS

Type:					Automatic. Telescopic 2 panel.

Finish:					Stainless steel finish (X02).

LANDING DOORS

Type:					Automatic. Telescopic 2 panel.

Finish:					Epoxy RAL 7044

Fire resistance

according to EN 81-58:			E120, EW60

CONTROL OPERATING PANEL

Model:					Column or FUSION with MP CARevolution

Finish:					Plastified steel

(Optional: Stainless steel (X02))

Button:	Mechanical plastic polycarbonate fireproof button lit using LEDs

(Optional: Mechanical stainless steel button with ring lighting)

Car indicator:				LCD and TFT display

Optional: 2-digit, 7-segment LED display.

Safety:					Emergency overhead lighting and telephone.

MP FLEX

___________________________________________________________________________mplifts.com

FLOOR OPERATING PANEL

Model:					P001, on door frame

Finish:					Stainless steel plate (X02)

Button:	Mechanical plastic polycarbonate fireproof button lit using LEDs.

(Optional: Mechanical stainless steel button with ring lighting)

Engraving:				Black logo (laser)

CONTROLLER

Type:					MP Selective or Universal.

Location:	On the highest floor for “S” series. Epoxy finish

ELECTRICAL INSTALLATION		Preassembled with “Plug & Play” connectors.

MACHINE	Gearless. Permanent maGO magnets with thermal safety cover to motor.

Rescue operation: Automatic rescue in addition to emergency electrical controller.

BUFFERS				In polyurethane with metal pedestal included

COLD-DRAWN / MACHINED		Cold-drawn / Machined

In accordance with ISO 7465

FIXINGS				Fixing brackets and plugs for concrete enclosure.

POWER

Power voltage: 				Three-phase 380 V

Optional: 220 V single-phase

Lighting: 				220 V

Frequency: 				50 Hz.